Safety Precautions Trivia Teacher Key

Question 1 (Worth 10 points):

Proper lockout/tag-out procedures were not followed. The power was restored without warning all affected persons. A person is being electrocuted (who should have had their own lock in place).
What is the emergency response? 
 
Correct Procedure:

1) Find a way to disconnect the power (Know where the emergency kill switch is located). If you don't know how to turn off the power source get a long current resistive item (wooden pole, PVC pipe) to remove the voltage source.
2) Send someone to call 911
3) Begin CPR and continue until help arrives.

Question 2 (Worth 10 points):

Proper lockout/tag-out procedures were not followed. The power was restored without warning all affected persons. A person is being electrocuted (who should have had their own lock in place).
What is the lockout tag-out procedure?

Correct Procedure:

1) Apply locks to power source after de-energizing.

2) Tag deactivated controls.

3) Tag de-energized equipment and circuits at all points where they can be energized.

Question 3 (Worth 5 points):

Construction is about to begin on a building with concrete forms and rebar.

What are the two safety fall protection guidelines that must be followed?

Correct Guidelines:

1) Use PFAS when working on formwork or rebar

2) Cover or cap protruding rebar

Question 4 (Worth 10 points):

The cover was removed from a breaker box and electrical parts are exposed.

What is the proper hazard control procedure?

Correct Procedure:

1) Guard live parts of electric equipment operating at 50 volts or more against accidental contact

2) Replace covers.

Question 5 (Worth 5 points):

You are using a portable tool with an extension cord that has a wire too small for the tool.

What are the requirements for a proper extension cord?

Correct Requirements:

1) Must be 3-wire type and designed for hard or extra-hard use.

2) Use fixed cords rather than flexible cords.

Question 6 (Worth 5 points):

What are 2 examples of PPE?

Correct Examples:

1) Proper foot protection (not tennis shoes)

2) Rubber insulating gloves, hoods, sleeves, matting, and blankets

3) Hard hat (insulated - nonconductive)

Question 7 (Worth 5 points):

What are three fall protection options?

Correct Answer:

1) Personal Fall Arrest System

2) Guardrails

3) Safety net

Question 8 (Worth 10 points):

Describe five situations where fall protection is needed?

Correct Answers:

1) Walkways & ramps

2) Open sides & edges

3) Holes

4) Concrete forms & rebar

5) Excavations

6) Roofs

7) Wall openings

8) Bricklaying

9) Residential Construction