## Module 02106-05
Plastic Pipe and Fittings

Lesson 2 of 2: Measuring, Cutting, and Joining, and Pipe Supports and Pressure Testing

This lesson is a combined classroom and lab session in which the students will learn how to measure, cut, and join plastic pipe as well as how to support plastic pipe and pressure-test the pipe.  Students must select appropriate personal protective equipment and then cut and join plastic pipe.  Additionally, they will select the correct hanger or support for the pipe for the application.  These tasks will fulfill Performance Task requirements.

Objectives

Upon completion of this lesson, the student should be able to:

- Describe the personal protective equipment required when cutting and joining plastic pipe.

- Properly measure, cut, and join plastic piping.

- Identify and determine the kinds of hangers and supports needed for plastic piping.

- Identify the various techniques used in hanging and supporting plastic piping.

Performance Requirements

  - Select appropriate personal protective equipment for cutting and joining plastic piping.  This corresponds to Performance Task 3.

  - Cut and join plastic pipes. This corresponds to Performance Task 4.

  - Select the correct hanger or support for the application.  This corresponds to Performance Task 5.

Reading Assignment

  - Module 02106, Sections 4 thru 6

Slide Presentation

  - Module 02106, Part 2 (Slides 17 thru 32)

Suggested Equipment/Materials

  - Samples of various types of plastic pipe and pipe fittings, cutting, joining, and reaming tools, solvent cement, personal protective equipment, and pipe support devices.

Suggested Student Activity

  - Under your supervision, students will practice cutting and joining plastic piping.

Testing

  - Module Review Test Questions 8 thru 18 for Sections 3.0.0. – 4.0.0, and Questions 1 thru 5 for Sections 5.0.0 – 6.0.0.

  - Module Trade Terms Quiz

  - Module Examination

Suggested Lab Activity

  - Students must select appropriate personal protective equipment and cut and join plastic piping.  Students must also select the correct hanger or support for plastic pipes.

Additional Resources

  - www.ppfahome.org (Plastic Pipe and Fitting Association) Information about thermoplastic piping systems.

  - Contren Connect Level 1Plumbng Annotated Instructors Guide (available from the NCCER)

SLIDE 17

  - Review the objectives to be covered in this lesson.  Ask students if they have any questions about the lesson or course objectives.

  - Describe and demonstrate how to cut plastic pipe.

  - Demonstrate how to ream a freshly cut plastic pipe.

  - Have a reamer available to pass around the class

SLIDE 18

  - Describe and demonstrate how to cut PVC and ABS pipe with cutting tools designed specifically to cut plastic pipe.

  - Allow students to practice cutting pipe using specialized cutting tools.

SLIDE 19

- Describe and demonstrate how to cut PVC and ABS pipe using a handsaw and miter box.

- Allow the students to practice cutting PVC and ABS pipe using a handsaw and miter box.

SLIDE 20

  - Describe how water supply and DWV fittings are joined using fittings that have gaskets or O-rings to provide a seal.

  - Describe the use of transition fittings when joining dissimilar pipes.

SLIDE 21

  - Describe how fusion fittings are used to fusion-weld plastic pipes.

SLIDE 22

  - Describe the solvent welding process used to join ABS, PVC, and CPVC plastic pipe and fittings.

SLIDE 23

  - Describe and demonstrate in detail, the steps required to join CPVC or PVC pipe using the solvent welding process.

  - Allow students to practice the joining procedure.  Ensure that appropriate personal protective equipment is worn by all participants.

SLIDE 24

  - Describe and demonstrate in detail, the steps required to join PVC bell-and-spigot pipe.

  - Allow students to practice the joining procedure.  Ensure that appropriate personal protective equipment is worn by all participants.

SLIDES 25 & 26

  - Describe and demonstrate in detail, the steps required to join PEX tubing using a crimp-ring system.

  - Slide 25 (Figure 18) shows the various tools needed, while slide 26 (Figure 19) shows the joining technique.

  - Allow students to practice the joining procedure.  Ensure that appropriate personal protective equipment is worn by all participants.

SLIDE 27

  - Describe and demonstrate in detail, the steps required to join PE tubing.

  - Allow students to practice the joining procedure.  Ensure that appropriate personal protective equipment is worn by all participants.

Have students answer Review Questions 8 thru 18 for Section 3.0.0 - 4.0.0.  Provide correct answers and remediation at the end of the quiz.

SLIDE 28

  - Explain the reasons why plastic piping must be properly supported.

  - Describe the various methods of supporting plastic pipes with hangers.

  - Have samples of pipe hangers available to pass around the class.

SLIDE 29

  - Explain that a variety of supports are also available to attach and support plastic pipes.

  - Discuss the types of supports used to attach pipe to metal structures.

  - Have samples of these supports available to pass around the class.

SLIDE 30

  - Discuss the types of supports used to provide support for horizontal pipe runs.

  - Have samples of these supports available to pass around the class.

SLIDE 31

  - Discuss the types of supports used to provide support for vertical pipe runs.

  - Have samples of these supports available to pass around the class.

SLIDE 32

  - Describe the reasons for pressure testing pipes and explain how it is done.

  - Explain that in some cases testing is done by simply sealing the system and applying municipal water pressure. In other cases, specs will require higher pressure, which is obtained by using a hydrostatic pump.

Have students answer Review Questions for Section 5.0.0 - 6.0.0 and the module Trade Terms Quiz.  Provide correct answers and remediation at the end of the quiz.

Students must select appropriate personal protective equipment and cut and join plastic piping.  Students must also select the correct hanger or support for plastic pipes.  These tasks correspond to Performance Tasks 3, 4, and 5 respectively.

At the completion of this session, provide a module review and then administer the Module Examination.  Students must achieve a score of at least 70% and have satisfactorily completed all lab exercises and/or Performance Testing requirements to receive credit for the module.