Basic Electronics

Use the Basic Electronic Worksheet to go with the Basic Electronic Power Point.

Directions: Fill in the blanks from the Basic Electronics PPT.

Basic Concept of a Circuit

- Three requirements of a complete circuit

- _Source_ of power

- _Load____ (something which uses that energy)

- Needs a ___Path__ to get the energy from source to load and back

- Millions of small charges called _electrons __ move through the circuit.

- When the switch is closed the __ electrons __ flow through the wires from the battery, to the switch, to the lamp, and back to the battery.

- What Charge is an electron?  _negative_

- When the circuit is complete or closed electrons flow through the wires from _ negative _ to __positive__.

- _Switch_ provides a simple way to open and close a circuit.

- Is a switch necessary to have a complete circuit?    _No___

Components: draw the symbols and fill in the blanks

| SPST Switch – Single Pole Single Throw | DPST Switch – Double Pole Single Throw |
| --- | --- |
| Momentary Switch | Open/Closed Switch |
| Wires Connected Symbols | or Wires Crossing (Not Connected) Symbols |

| Lamp | Speaker |
| --- | --- |
| Capacitor | Electrons are stored inside the capacitor causing it to act like a battery Capacitance is measured in microfarads Plates are the conductors inside the capacitor. Electrons move around the plates causing storage of energy that continues flowing even after all power has been disconnected. Dielectric are the insulators inside the capacitor. Discharging capacitors Before working with a capacitor be sure it is discharged. Touch a probe to each capacitor terminal for discharge. Substituting capacitors Replace the capacitors with exact voltage rating. If impossible the voltage rating must be greater If a lower rating is used the circuit will result in damage. |
| Resistors (R) | Opposes the flow of current (I) Can be used as a fuse in a circuit R are not polarity sensitive Measured in Ohms |
| Variable Resistor: opposes the flow of current (I) Designers use the pot to find the correct current (I) for a circuit AB + BC = AC | Potentiometer |
| Photocell | Look at the photocell’s symbol & tell how the component operates. Squiggly lines mean: resistance: opposing the flow of (I) current Arrows pointing in means: the light comes from outside the component |
| One directional gate Has a anode and cathode | Diode |
| LED | LED: Light Emitting Diode Arrows pointing out means: light comes from the component Component symbol in the middle means: one directional gate |
| SCR | SCR -- Silicon Controlled Rectifier Voltage (E) to the gate turns the SCR on |
| Transistor: amplification of signal |
| Transistor – NPN | Transistor – PNP |
| IC – Integrated Circuit 555 alternates from turning the voltage on & off 555 produces a square wave at its output Frequency is step by the attached resistors & capacitor Circle or dot on the IC marks pin ONE | 555 Timer -- IC |
| Cell | two or more cells Battery |

- If one resistor or component _burns_ out the circuit will be open and not operational.

- Total resistance = 1.2K + 100 + 360

= 1660 ohms

- Circuit which contains two or more paths for electrons to flow from a common voltage source

- If one resistor burns out the other resistors will be closed and operational

1

- Total resistance = 1/1.2K + 1/100 + 1/360

= 73.46 ohms

| Draw an open Circuit using: cell switch lamp 1k ohm resistor | Draw a closed Circuit using: battery switch lamp 1k ohm resistor |
| --- | --- |

Directions:  Complete the following questions on your own.     Score:  __________

- List four items of electricity in your everyday living.

  - Answers will vary

  - _____________________________________________________

  - _____________________________________________________

  - _____________________________________________________

- The necessary part of a completed circuit includes:

  - Source, path, and load

  - Electricity and devices

  - Components and wires

- The purpose of a switch is to:

  - Add components so the cost will increase

  - Allows easier opening and closing of the circuit

  - Must have a switch so the circuit can become closed

- The movement of electricity is from:

  - Negative to positive

  - Positive to negative

  - Neutral to negative

- In a circuit with a battery, the electrons flow:

  - Out of the positive terminal

  - Out of the negative terminal

  - From the battery acid

- My flashlight has (two) 1.5-volt power sources.  What should I call them cells or batteries?  BATTERY

- Draw symbols for each electrical component.

| Cell See above | Battery | Lamp | Wires crossing | Wires connected |
| --- | --- | --- | --- | --- |

Directions:  Match the words to the correct definition.

| _C_ Chemical Energy G Load J Photocell E Diode F Insulator B Capacitor K Resistance L Series Circuit I Parallel Circuit N Solder M Schematic A Batteries D Conductors H Multi Meter | A two or more cell are combined a battery is formed B Two conductors separated by an insulator or dielectric used to store an electrical charge C. electricity is generated through the use of chemicals and their reaction with other materials D. An item or material, which is used to carry current; a wire E. allows electrons to follow in one direction and blocking flow from the other direction; commonly know as a one way directional gate F. object that will not allow current to flow G. device that is being driven by the source of power; absorbs the power from the supply voltage and converts it to heat, light, etc; resistance connected across a circuit that determines the current flow and energy used H. electrical measuring device (I, E, & R) I. circuit which contains two or more paths for electrons to flow from a common voltage source J. cell which will change its resistance when hit by light K. Opposition to the flow of current L circuit in which components are connect from end to end, and the current must flow through each tone in sequence to complete its path M. electrical diagram that shows components as symbols and electrical connections of components to each other N. alloy of tin and lead used for providing a low resistance electrical connection which is also mechanically strong |
| --- | --- |

# Text boxes

A

B

anode

cathode

(+)‏

(-)‏

Anode

(+)‏

Cathode

(-)‏

C

A

Gate

1

2

3

4

6

8

5

7

(-)‏

(+)‏