Transportaion Logistcal Operations and Support: Electrical System Design

CTAE Resource Network

Unit 4 Starting System Testing Starting Starters

Starter – An electric motor which uses a geardrive to crank (start) the engine.

Armature Loop – The revolving part in an alternator or motor. The moving part in a relay or horn.

Commutator Segments – A series of copper bars connected to an armature winding. The bars are insulated from each other and from the armature.

Starter Pinion Gear – A small gear on the end of the starter shaft that engages and turns the flywheel ring gear.

Overrunning Clutch Drive – A clutch mechanism that will drive in one direction and slip in the other.

Solenoid – An electrically operated magnetic device used to operate some unit. An iron core is place inside a coil. When electricity is applied to the coil, the iron core centers itself in the coil and, as a result, it will exert some force on anything or rear of the vehicle.

Reduction Gear –  A gear that increases torque by reducing the speed of a driven shaft in relation to the driving shaft.