PATHWAY:  Transportation Logistical Operations and Support

COURSE:  Foundations of Transportation and Logistics

UNIT 15 : Ignition Systems Diagnosis and Repair

Introduction

Annotation:

Through the use of lecture, multimedia resources, demonstration, group activities, and hands-on lab work the instructor will assist the student to safely and properly test automotive engine performance systems and components. Students will be instructed in diagnosis and testing of engine performance systems. Safety and environmental responsibility will be covered in detail. Safe, clean procedures using recommended service tools will be included in instruction.

Grade(s):

| x | 9th |
| --- | --- |
| x | 10th |
| x | 11th |
| x | 12th |

Time:

5 (2 hour periods)

Author:

Sonny Reeves sreeves.hutchingscc@bibb.k12.ga.us  www.autoteacher.net

Additional Author(s):

Students with Disabilities:

For students with disabilities, the instructor should refer to the student's IEP to be sure that the accommodations specified are being provided. Instructors should also familiarize themselves with the provisions of Behavior Intervention Plans that may be part of a student's IEP. Frequent consultation with a student's special education instructor will be beneficial in providing appropriate differentiation.

Focus Standards

GPS Focus Standards:

ACT-FTL-10: Determines problem-solving strategies.

GPS Academic Standards:

ELA12W3, The student uses research and technology to support writing.

SPS10, Students will investigate the properties of electricity and magnetism.

NATEF Standards:

VIII.	 ENGINE PERFORMANCE 	C. Ignition System Diagnosis and Repair

1. Diagnose ignition system related problems such as no-starting, hard starting, engine misfire, poor

driveability, spark knock, power loss, poor mileage, and emissions concerns; determine necessary action.

2. Inspect and test ignition primary and secondary wiring and solid state components; test ignition coil(s);

perform necessary action.

3. Inspect and test crank shaft or camshaft sensors or triggering devices; perform necessary action

4. Inspect, test and/or replace ignition control module (ICM)/powertrain/engine control module (PCM/ECM); reprogram as needed.

NATEF Academic Standards:

SC041 Applies/Uses Laboratory Techniques Safety

- The technician follows all safety regulations and applicable procedures while performing the task.

LA023 Applies/Uses Study Habits/Methods Skimming/Scanning

- The technician will visually skim or scan the manufacturer's service manuals or data bases to identify information that is related to any unfamiliar system under review, then study the applicable information with the intensity necessary for the situation.

LA035 Attends Directions/Task

- The technician attends to written and oral directions that relate to the engine repair task or system under study.

MA271 Determines Proper Operation

- When comparing system measurements to manufacturer's specifications, the technician can determine the proper sequence of arithmetic operations to arrive at a solution for comparison to specifications.

Understandings & Goals

Enduring Understandings:

Students will understand that high voltage secondary current is dependant on quality of low voltage sensors and controls and that proper timing of engine functions is necessary for efficient operation of internal combustion engines operation.

Essential Questions:

What are the safety concerns for the technician in engine performance ignition system testing?
Why are clean, orderly work habits important?
What are the Health and Safety regulations for working with engine performance test equipment?
Why is the delivery of good spark and proper timing important to optimum engine performance?
What are types of engine performance ignition system failures?

Knowledge from this Unit:

Students will learn about computer based and printed material along with scientific reasoning that will allow them to perform adjustment, diagnosis, and repair of automotive systems.

Skills from this Unit:

- Identify the safe use of chemicals used in engine performance.

- Identify the safe use of hand tools used in engine performance.

- Identify the safe use of power tools used in engine performance.

- Identify the safe use of protective clothing and equipment for working in engine performance.

- Identify the safe use of fire protection equipment for working in engine performance.

- Identify the safe use of shop equipment for working in engine performance.

- Follow Environmental Protection Agency (EPA) and occupational Safety and Health Act (OSHA) 	regulations for working in engine performance.

Assessment(s)

Assessment Method Type: Select one or more of the following. Please consider the type(s) of differentiated instruction you will be using in the classroom.

|  | Pre-test |
| --- | --- |
|  | Objective assessment - multiple-choice, true- false, etc. |
|  | __ Quizzes/Tests __ Unit test |
|  | Group project |
|  | Individual project |
| x | Self-assessment - May include practice quizzes, games, simulations, checklists, etc. |
|  | _x_ Self-check rubrics __ Self-check during writing/planning process __ Journal reflections on concepts, personal experiences and impact on one’s life __ Reflect on evaluations of work from teachers, business partners, and competition judges __ Academic prompts _x_ Practice quizzes/tests |
|  | Subjective assessment/Informal observations |
|  | __ Essay tests __ Observe students working with partners __ Observe students role playing |
| x | Peer-assessment |
|  | __ Peer editing & commentary of products/projects/presentations using rubrics _x_ Peer editing and/or critiquing |
|  | Dialogue and Discussion |
|  | __ Student/teacher conferences __ Partner and small group discussions __ Whole group discussions __ Interaction with/feedback from community members/speakers and business partners |
|  | Constructed Responses |
|  | __ Chart good reading/writing/listening/speaking habits __ Application of skills to real-life situations/scenarios |
|  | Post-test |

Assessment(s) Title:

Work Sheet and assessment checklist for engine timing

Assessment(s) Description/Directions:

Work Sheet and assessment checklist can be used for assessment of student learning and practice of the task. Work sheet is detailed and self descriptive. Work Sheet can be used for student practice. Work sheet and assessment checklist can be modified for use in your lab.

Attachments for Assessment(s):

Guide and Video in Web Resources

Work Sheet and assessment checklist for engine timing

http://www.cdxetextbook.com/PDF/ws/igntime_WS.pdf

http://www.cdxetextbook.com/PDF/ac/igntime_AC.pdf

Learning Experiences

Instructional planning: Include lessons, activities and other learning experiences in this section with a brief description of the activities to ensure student acquisition of the knowledge and skills addressed in the standards. Complete the sequence of instruction for each lesson/task in the unit.

Sequence of Instruction

1.  Identify the Standards. Standards should be posted in the classroom for each lesson.

2.  Review Essential Questions.

3.  Identify and review the unit vocabulary.

4.  Assessment Activity.

Step 1

Introduce students to engine performance system and component testing with review of safety in the use of electrical testing. Review operation of internal combustion engine.

Warn students of the dangers associated with live engine service. Refer to previous lesson on shop safety. Guide students to access factory service information for timing specifications on electronic service information system. Explain the importance of research for factory solutions to a service problem with engine performance.

Step:  2

Review operation of the engine and the related systems. Discuss operation and design of engine performance systems. Discuss various ways engine ignition timing is controlled. Demonstrate basic test procedures. Caution students on safe use of test equipment on running engines.

Web Resources for Step 2

Title: Theory and Operation of Engine Ignition Systems
URL: http://www.autoshop101.com
Annotation: Visit Web site for theory and operation of systems to be tested.

Title: Theory and Operation of Engines
URL: http://science.howstuffworks.com/engines-channel.htm
Annotation: Great resource for theory and operation of engine performance systems.

Step:  3

Use a set up shop vehicle(s) to demonstrate the procedures to check and adjust ignition timing. Set up several vehicles or modules that students can use to practice checking ignition timing. Have a selection of sensors and demonstrate the control of timing by the ECM.  Use a DSO and scanner to see the timing change. Allow students to practice checking engine ignition timing. Stress proper test procedures with attached work sheet.

Attachments for Step 3

Title: Checking Engine Performance Concerns, Ignition Timing

FileName: Engine Timing Adjustment

URL: http://vodpod.com/watch/1521341-car-hub-tv-how-to-set-your-timing
Description: Use worksheet to guide students in this exercise. Work sheet can be modified to meet student and teacher needs.

Step:  4

Prepare a “problem” on the vehicle and demonstrate finding the concern. Discuss service problems and solutions of the different problems technicians may encounter. Demonstrate effect of incorrect timing.

Step:  5

Allow students to practice the procedures with instructor observation. Guide lab exercise with job sheet.

Step:  6

Allow students to practice and complete job sheets and performance tests. Use job sheet as guide for lab exercise and performance test as the rubric for this task.

Web Resources for Step 6

Title: Northwest Training Consortium
URL: http://www.careersnet.org/automotive/engine.htm

Annotation: Visit web site for job sheets, Power Point presentations and more web links for engine performance testing.

Title: Checking Secondary Ignition, Changing spark plugs
URL: http://www.expertvillage.com/video/27224_cars-care-spark-plugs.htm
Annotation: Free online textbook, Video presentations and more for engine performance testing.

Attachments for Step 6

Title: Performance Test Ignition Timing

FileName: https://www.autoteacher.net/Performance_Tests_6XEQ.html

Description: Use attached performance test for the assessment of this task. Can the student perform the task? These examples may be modified to meet teacher and student needs.

Attachments for Learning Experiences: Please list.

Notes & Reflections:

Shop Safety issues are to be reviewed and stressed in this lesson. Student safety in the handling of flammables and highly volatile gasoline is imperative. Students will identify the importance of safe tool and equipment use. Emphasize importance of correct testing procedures in the lab exercise. Review the safe handling of live engines in lab.

Culminating Performance Task (Optional)

# Culminating Unit Performance Task Title:

# EP PT Ignition14

Culminating Unit Performance Task Description/Directions/Differentiated Instruction:

The Performance Test Rubric for this unit can be modified to suit the instructor needs. Students can work in teams during practice then use the performance test for peer review of each others skill level then present the document to the instructor for final assessment. Instructor can perform observation and assessment of individual students in lab using the performance test.

Attachments for Culminating Performance Task:

URL for download

https://autoteacher.net/uploads/PT_CS_TimingChecks_4.doc

Unit Resources

Web Resources:

http://www.autoshop101.com/  The site is a electrical and engine performance course based on Toyota technical information

Electronic control unit settings Detailed example of engine timing control

Assessment guide

http://www.cdxetextbook.com/PDF/ac/igntime_AC.pdf

Video sequence

http://www.cdxetextbook.com/engines/motivePower/4gasEng/engcycle_cable.html

Performance Tests and teacher helps;

www.autoteacher.net

Attachment(s):

Materials & Equipment:

1. O-Scope(Digital storage oscilloscope), scanners, DMM, timing light and specific engine analysis equipment.

2. Set up several vehicles with working engine performance systems or modules.

3. Basic hand tools, and special service tools for vehicles being used.

4. Reference materials such as factory service manuals, electronic service information.

5. Provide safety glasses, protective clothing and cleaning supplies.

6. Modules, sensors and control devices for bench testing

What 21st Century Technology was used in this unit:

Top of Form

|  | Slide Show Software |  | Graphing Software |  | Audio File(s) |
| --- | --- | --- | --- | --- | --- |
|  | Interactive Whiteboard |  | Calculator |  | Graphic Organizer |
|  | Student Response System |  | Desktop Publishing | x | Image File(s) |
|  | Web Design Software |  | Blog |  | Video |
|  | Animation Software |  | Wiki |  | Electronic Game or Puzzle Maker |
|  | Email | x | Website |  |  |

Bottom of Form

# Text boxes

Transportation